## Slide 1: Design & Verification of Low-Power Perceptron Based AI Engine
Project Presented:
Mohammed Moienuddin Ali.S.A
Packya Muthukumar.M
Pradeep Palaniselvam.T
Vigneshkannan.R
Guided By:
Mrs. J. Nargis (Asst. Professor)
GOVERNMENT COLLEGE OF ENGINEERING, BARGUR
DEPARTMENT OF ELECTRONICS & COMMUNICATION ENGINEERING
20.04.2026 (MONDAY)

## Slide 2: Table of contents 01 04 02 05 03 06
Testbench • Simulation
Motivation • Objective
System • Perceptron
Synthesis • Timing • Power
Modules • UART
Enhancements
Introduction
Architecture
RTL Design
Verification
Analysis
Future Work

## Slide 3: Introduction 01
Edge AI applications require low-power and low-latency inference. Hardware acceleration enables efficient implementation of neural computation compared to software execution.

## Slide 4: Project Motivation
Artificial Intelligence inference is increasingly required in edge devices such as IoT nodes, wearable systems, and embedded controllers. Conventional software-based implementations on CPUs or GPUs introduce higher latency and power consumption, making them unsuitable for resource-constrained environments. Hardware acceleration offers parallelism, low latency, and energy efficiency, making it an attractive platform for deploying lightweight neural network models.
A perceptron-based architecture provides a simple yet effective hardware-friendly solution for binary classification tasks. Therefore, this project focuses on designing a low-power perceptron-based AI engine implemented in hardware for efficient real-time inference.

## Slide 5: Project Objective
Design a perceptron-based AI inference engine using Verilog HDL
Implement UART-based feature input from host system
Perform hardware-based classification on FPGA
Optimize architecture for low-power operation
Verify functionality using simulation and synthesis reports
Demonstrate real-time prediction output

## Slide 6: Architecture 02
The system receives feature data through UART, processes it using a perceptron computation core, and generates a classification output through an activation layer.

## Slide 7: System Architecture
Laptop
UART RX Feature Input
Packet Parser Feature Extraction
Perceptron Core MAC Operation
Activation Layer Decision
UART TX Output
Prediction Output

## Slide 8: Perceptron Model
The perceptron computes a weighted sum of features and applies thresholding to produce a binary classification output.
y = 1 if ( Σ (wi × xi) + b ) ≥ threshold
y = 0 otherwise
The perceptron is a single-layer neural model used for binary classification. It computes a weighted sum of input features followed by bias addition. A threshold-based activation function is applied to generate the final prediction output.
x0 – w0
x1 – w1
…
x7 – w7
Sum + Bias Activation Output

## Slide 9: RTL Design 03
The design is implemented using modular Verilog blocks including communication, datapath, and control logic integrated into a top-level architecture.

## Slide 10: RTL Design Overview
AI System top module integrated
Perceptron
core
Activation
layer
UART
Transmitter
Communication
Top module
UART Receiver
Packet Parser

## Slide 11: RTL Modules
Handles UART reception and groups incoming bytes into feature packets
Applies threshold logic to generate binary prediction
Performs weighted sum computation of input features
Transmits prediction result back to host system
(A.3) comm_top
(A.1) perceptron_core
(A.2) activation_layer
(A.4) uart_tx
(A) ai_system_top
Integrates all modules into complete AI inference pipeline
(A.3.1) uart_rx
(A.3.2) packet_parser
Receives serial data and converts it into parallel feature values
Converts the parallel feature values into a packet through fsm

## Slide 12: UART Communication
Receives feature data byte-by-byte
Operates at 115200 baud rate (8N1 format)
UART used for serial communication with host system
Converts serial input into parallel feature values
Transmits prediction result back via UART
Baud Rate : 115200
Data Bits : 8
Parity : None
Stop Bits : 1
Clock : 50 MHz (configured)
Key Parameters

## Slide 13: Verification 04
Simulation waveforms confirm correct UART reception, feature parsing, weighted computation, and final classification output.

## Slide 14: Testbench
A Verilog testbench is developed to verify the functionality of the AI system. It generates clock and reset signals and simulates UART input by sending feature data as serial packets. The system response is observed to ensure correct feature extraction, computation, and prediction output.
Clock Generator
Reset Logic
UART Stimulus (send_byte)
Feature Packet Input
Output Monitoring
Test Packet Example
Start : 0xAA
Features : 12, 8, -3, 4, 6, 2, 9, -1
End : 0x55

## Slide 15: Testbench Code Snippet
task send_byte;
input [7:0] data;
integer i;
begin
rx = 0; #(BIT_PERIOD);
for (i = 0; i < 8; i = i + 1) begin
rx = data[i];
#(BIT_PERIOD);
end
rx = 1;
#(BIT_PERIOD);
end
endtask

## Slide 16: Simulation

## Slide 18: Analysis 05

## Slide 19: Vivado Synthesis Results
The RTL design is synthesized using Xilinx Vivado to evaluate hardware resource utilization. The synthesis results show efficient usage of LUTs, registers, and DSP slices, indicating that the perceptron-based AI engine is suitable for FPGA implementation.
Utilization Report

## Slide 20: Vivado Synthesis Results
DSP usage → AI computation
Low LUT count → efficient design
Key Observations (Based on Utilization Report)
Resource | Usage
LUTs | 218(~1%)
Registers | 224(~1%)
I/O | 15
DSP/BRAM | Minimal/None

## Slide 21: Timing Analysis
WNS > 0 → Timing met
TNS = 0 → No violations
Inference latency ≈ ~10 clock cycles
Suitable for real-time applications
“All User specified timing constraints are met.”

## Slide 22: Low-power considerations
Low resource utilization (~1% LUTs, Registers)
Sequential MAC operation reduces switching activity
No large memory blocks (BRAM not used)
Minimal combinational complexity
Suitable for low-power edge AI applications
Uses sequential processing instead of parallel heavy logic
Only active during computation (not always switching)
Lightweight design → less power consumption
Dynamic Power ∝ Switching Activity × Capacitance × Frequency²
The lightweight architecture ensures energy-efficient AI inference suitable for edge devices.

## Slide 23: Low-power considerations
Dynamic Power ∝ Switching Activity × Capacitance × Frequency²

## Slide 24: Future Work 05

## Slide 25: Enhancements
From Single Neuron → Neural Network
From Fixed Weights → Trainable / Configurable System
From Prototype → Real Product
The current design can be extended to support more complex neural network architectures by incorporating multiple perceptron layers. Future enhancements include programmable weights, memory integration, pipeline optimization, and real-time deployment for practical edge AI applications.

## Slide 26: Conclusion
This project successfully demonstrates the design and verification of a perceptron-based AI decision engine. The system is verified through simulation and achieves efficient resource utilization with timing closure. The lightweight and scalable architecture makes it suitable for low-power edge AI applications.
Real-time hardware validated ✔
Scalable architecture ✔
Industry-relevant design ✔

## Slide 27
Interaction session!
Any queries?

## Slide 28: Thank You!